## Slide 1
PC Architecture(PCA190802)
CO1: Identify various architecture of motherboard and chipset
CO2: Demonstrate architecture of 8085 microprocessor
CO3: Interpret the working of different storage devices and its interfaces
CO4: Troubleshoot Maintenance of PC and test power supply

## Slide 2: INSTRUCTION SET OF 8085

## Slide 3: Instruction Set of 8085
An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
The entire group of instructions that a microprocessor supports is called Instruction Set.
8085 has 246 instructions.
Each instruction is represented by an 8-bit binary value.
These 8-bits of binary value is called Op-Code or Instruction Byte.

## Slide 4: Classification of Instruction Set
Data Transfer Instruction
Arithmetic Instructions
Logical Instructions
Branching Instructions
Control Instructions

## Slide 5: Data Transfer Instructions
These instructions move data between registers, or between memory and registers.
These instructions copy data from source to destination.
While copying, the contents of source are not modified.

## Slide 6: Data Transfer Instructions
Opcode | Operand | Description
MOV | Rd, Rs M, Rs Rd, M | Copy from source to destination.
This instruction copies the contents of the source register into the destination register.
The contents of the source register are not altered.
If one of the operands is a memory location, its location is specified by the contents of the HL registers.
Example: MOV B, C or MOV B, M

## Slide 7: Data Transfer Instructions
Opcode | Operand | Description
MVI | Rd, Data M, Data | Move immediate 8-bit
The 8-bit data is stored in the destination register or memory.
If the operand is a memory location, its location is specified by the contents of the H-L registers.
Example: MVI B, 57H or MVI M, 57H

## Slide 8: Data Transfer Instructions
Opcode | Operand | Description
LDA | 16-bit address | Load Accumulator
The contents of a memory location, specified by a 16-bit address in the operand, are copied to the accumulator.
The contents of the source are not altered.
Example: LDA 2034H

## Slide 9: Data Transfer Instructions
Opcode | Operand | Description
LDAX | B/D Register Pair | Load accumulator indirect
The contents of the designated register pair point to a memory location.
This instruction copies the contents of that memory location into the accumulator.
The contents of either the register pair or the memory location are not altered.
Example: LDAX B

## Slide 10: Data Transfer Instructions
Opcode | Operand | Description
LXI | Reg. pair, 16-bit data | Load register pair immediate
This instruction loads 16-bit data in the register pair.
Example: LXI H, 2034 H

## Slide 11: Data Transfer Instructions
Opcode | Operand | Description
LHLD | 16-bit address | Load H-L registers direct
This instruction copies the contents of memory location pointed out by 16-bit address into register L.
It copies the contents of next memory location into register H.
Example: LHLD 2040 H

## Slide 12: Data Transfer Instructions
Opcode | Operand | Description
STA | 16-bit address | Store accumulator direct
The contents of accumulator are copied into the memory location specified by the operand.
Example: STA 2500 H

## Slide 13: Data Transfer Instructions
Opcode | Operand | Description
STAX | Reg. pair | Store accumulator indirect
The contents of accumulator are copied into the memory location specified by the contents of the register pair.
Example: STAX B

## Slide 14: Data Transfer Instructions
Opcode | Operand | Description
SHLD | 16-bit address | Store H-L registers direct
The contents of register L are stored into memory location specified by the 16-bit address.
The contents of register H are stored into the next memory location.
Example: SHLD 2550 H

## Slide 15: Data Transfer Instructions
Opcode | Operand | Description
XCHG | None | Exchange H-L with D-E
The contents of register H are exchanged with the contents of register D.
The contents of register L are exchanged with the contents of register E.
Example: XCHG

## Slide 16: Data Transfer Instructions
Opcode | Operand | Description
SPHL | None | Copy H-L pair to the Stack Pointer (SP)
This instruction loads the contents of H-L pair into SP.
Example: SPHL

## Slide 17: Arithmetic Instructions
These instructions perform the operations like:
  Addition
  Subtract
  Increment
  Decrement

## Slide 18: Addition
Any 8-bit number, or the contents of register, or the contents of memory location can be added to the contents of accumulator.
The result (sum) is stored in the accumulator.
No two other 8-bit registers can be added directly.
Example: The contents of register B cannot be added directly to the contents of register C.

## Slide 19: Subtraction
Any 8-bit number, or the contents of register, or the contents of memory location can be subtracted from the contents of accumulator.
The result is stored in the accumulator.
Subtraction is performed in 2’s complement form.
If the result is negative, it is stored in 2’s complement form.
No two other 8-bit registers can be subtracted directly.

## Slide 20: Increment / Decrement
The 8-bit contents of a register or a memory location can be incremented or decremented by 1.
The 16-bit contents of a register pair can be incremented or decremented by 1.
Increment or decrement can be performed on any register or a memory location.

## Slide 21: Arithmetic Instructions
Opcode | Operand | Description
ADD | R M | Add register or memory to accumulator
The contents of register or memory are added to the contents of accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of the addition.
Example: ADD B or ADD M

## Slide 22: Arithmetic Instructions
Opcode | Operand | Description
ADC | R M | Add register or memory to accumulator with carry
The contents of register or memory and Carry Flag (CY) are added to the contents of accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of the addition.
Example: ADC B or ADC M

## Slide 23: Arithmetic Instructions
Opcode | Operand | Description
ADI | 8-bit data | Add immediate to accumulator
The 8-bit data is added to the contents of accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of the addition.
Example: ADI 45 H

## Slide 24: Arithmetic Instructions
Opcode | Operand | Description
ACI | 8-bit data | Add immediate to accumulator with carry
The 8-bit data and the Carry Flag (CY) are added to the contents of accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of the addition.
Example: ACI 45 H

## Slide 25: Arithmetic Instructions
Opcode | Operand | Description
DAD | Reg. pair | Add register pair to H-L pair
The 16-bit contents of the register pair are added to the contents of H-L pair.
The result is stored in H-L pair.
If the result is larger than 16 bits, then CY is set.
No other flags are changed.
Example: DAD B

## Slide 26: Arithmetic Instructions
Opcode | Operand | Description
SUB | R M | Subtract register or memory from accumulator
The contents of the register or memory location are subtracted from the contents of the accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of subtraction.
Example: SUB B or SUB M

## Slide 27: Arithmetic Instructions
Opcode | Operand | Description
SBB | R M | Subtract register or memory from accumulator with borrow
The contents of the register or memory location and Borrow Flag (i.e. CY) are subtracted from the contents of the accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of subtraction.
Example: SBB B or SBB M

## Slide 28: Arithmetic Instructions
Opcode | Operand | Description
SBI | 8-bit data | Subtract immediate from accumulator with borrow
The 8-bit data and the Borrow Flag (i.e. CY) is subtracted from the contents of the accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of subtraction.
Example: SBI 45 H

## Slide 29: Arithmetic Instructions
Opcode | Operand | Description
INR | R M | Increment register or memory by 1
The contents of register or memory location are incremented by 1.
The result is stored in the same place.
If the operand is a memory location, its address is specified by the contents of H-L pair.
Example: INR B or INR M

## Slide 30: Arithmetic Instructions
Opcode | Operand | Description
INX | R | Increment register pair by 1
The contents of register pair are incremented by 1.
The result is stored in the same place.
Example: INX H

## Slide 31: Arithmetic Instructions
Opcode | Operand | Description
DCR | R M | Decrement register or memory by 1
The contents of register or memory location are decremented by 1.
The result is stored in the same place.
If the operand is a memory location, its address is specified by the contents of H-L pair.
Example: DCR B or DCR M

## Slide 32: Arithmetic Instructions
Opcode | Operand | Description
DCX | R | Decrement register pair by 1
The contents of register pair are decremented by 1.
The result is stored in the same place.
Example: DCX H

## Slide 33: Logical Instructions
These instructions perform logical operations on data stored in registers, memory and status flags.
The logical operations are:
  AND
  OR
  XOR
  Rotate
  Compare
  Complement

## Slide 34: AND, OR, XOR
Any 8-bit data, or the contents of register, or memory location can logically have
  AND operation
  OR operation
  XOR operation
with the contents of accumulator.
The result is stored in accumulator.

## Slide 35: Rotate
Each bit in the accumulator can be shifted either left or right to the next position.

## Slide 36: Compare
Any 8-bit data, or the contents of register, or memory location can be compares for:
  Equality
  Greater Than
  Less Than
with the contents of accumulator.
The result is reflected in status flags.

## Slide 37: Complement
The contents of accumulator can be complemented.
Each 0 is replaced by 1 and each 1 is replaced by 0.

## Slide 38: Logical Instructions
Opcode | Operand | Description
CMP | R M | Compare register or memory with accumulator
The contents of the operand (register or memory) are compared with the contents of the accumulator.
Both contents are preserved .
The result of the comparison is shown by setting the flags of the PSW as follows:

## Slide 39: Logical Instructions
Opcode | Operand | Description
CMP | R M | Compare register or memory with accumulator
if (A) < (reg/mem): carry flag is set
if (A) = (reg/mem): zero flag is set
if (A) > (reg/mem): carry and zero flags are reset.
Example: CMP B or CMP M

## Slide 40: Logical Instructions
Opcode | Operand | Description
CPI | 8-bit data | Compare immediate with accumulator
The 8-bit data is compared with the contents of accumulator.
The values being compared remain unchanged.
The result of the comparison is shown by setting the flags of the PSW as follows:

## Slide 41: Logical Instructions
Opcode | Operand | Description
CPI | 8-bit data | Compare immediate with accumulator
if (A) < data: carry flag is set
if (A) = data: zero flag is set
if (A) > data: carry and zero flags are reset
Example: CPI 89H

## Slide 42: Logical Instructions
Opcode | Operand | Description
ANA | R M | Logical AND register or memory with accumulator
The contents of the accumulator are logically ANDed with the contents of register or memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result of the operation.
CY is reset and AC is set.
Example: ANA B or ANA M.

## Slide 43: Logical Instructions
Opcode | Operand | Description
XRA | R M | Exclusive OR register or memory with accumulator
The contents of the accumulator are XORed with the contents of the register or memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result of the operation.
CY and AC are reset.
Example: XRA B or XRA M.

## Slide 44: Logical Instructions
Opcode | Operand | Description
ORA | R M | Logical OR register or memory with accumulator
The contents of the accumulator are logically ORed with the contents of the register or memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result.
CY and AC are reset.
Example: ORA B or ORA M.

## Slide 45: Logical Instructions
Opcode | Operand | Description
ORI | 8-bit data | Logical OR immediate with accumulator
The contents of the accumulator are logically ORed with the 8-bit data.
The result is placed in the accumulator.
S, Z, P are modified to reflect the result.
CY and AC are reset.
Example: ORI 86H.

## Slide 46: Logical Instructions
Opcode | Operand | Description
XRA | R M | Logical XOR register or memory with accumulator
The contents of the accumulator are XORed with the contents of the register or memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result of the operation.
CY and AC are reset.
Example: XRA B or XRA M.

## Slide 47: Logical Instructions
Opcode | Operand | Description
XRI | 8-bit data | XOR immediate with accumulator
The contents of the accumulator are XORed with the 8-bit data.
The result is placed in the accumulator.
S, Z, P are modified to reflect the result.
CY and AC are reset.
Example: XRI 86H.

## Slide 48: Logical Instructions
Opcode | Operand | Description
RLC | None | Rotate accumulator left
Each binary bit of the accumulator is rotated left by one position.
Bit D7 is placed in the position of D0 as well as in the Carry flag.
CY is modified according to bit D7.
S, Z, P, AC are not affected.
Example: RLC.

## Slide 49: Logical Instructions
Opcode | Operand | Description
RRC | None | Rotate accumulator right
Each binary bit of the accumulator is rotated right by one position.
Bit D0 is placed in the position of D7 as well as in the Carry flag.
CY is modified according to bit D0.
S, Z, P, AC are not affected.
Example: RRC.

## Slide 50: Logical Instructions
Opcode | Operand | Description
CMA | None | Complement accumulator
The contents of the accumulator are complemented.
No flags are affected.
Example: CMA.

## Slide 51: Logical Instructions
Opcode | Operand | Description
CMC | None | Complement carry
The Carry flag is complemented.
No other flags are affected.
Example: CMC.

## Slide 52: Logical Instructions
Opcode | Operand | Description
STC | None | Set carry
The Carry flag is set to 1.
No other flags are affected.
Example: STC.

## Slide 53: Branching Instructions
The branching instruction alter the normal sequential flow.
These instructions alter either unconditionally or conditionally.

## Slide 54: Branching Instructions
Opcode | Operand | Description
JMP | 16-bit address | Jump unconditionally
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand.
Example: JMP 2034 H.

## Slide 55: Branching Instructions
Opcode | Operand | Description
Jx | 16-bit address | Jump conditionally
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand based on the specified flag of the PSW.
Example: JZ 2034 H.

## Slide 56: Jump Conditionally
Opcode | Description | Status Flags
JC | Jump if Carry | CY = 1
JNC | Jump if No Carry | CY = 0
JP | Jump if Positive | S = 0
JM | Jump if Minus | S = 1
JZ | Jump if Zero | Z = 1
JNZ | Jump if No Zero | Z = 0
JPE | Jump if Parity Even | P = 1
JPO | Jump if Parity Odd | P = 0

## Slide 57: Branching Instructions
Opcode | Operand | Description
CALL | 16-bit address | Call unconditionally
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand.
Before the transfer, the address of the next instruction after CALL (the contents of the program counter) is pushed onto the stack.
Example: CALL 2034 H.

## Slide 58: Call Conditionally
Opcode | Description | Status Flags
CC | Call if Carry | CY = 1
CNC | Call if No Carry | CY = 0
CP | Call if Positive | S = 0
CM | Call if Minus | S = 1
CZ | Call if Zero | Z = 1
CNZ | Call if No Zero | Z = 0
CPE | Call if Parity Even | P = 1
CPO | Call if Parity Odd | P = 0

## Slide 59: Control Instructions
The control instructions control the operation of microprocessor.

## Slide 60: Control Instructions
Opcode | Operand | Description
NOP | None | No operation
No operation is performed.
The instruction is fetched and decoded but no operation is executed.
Example: NOP

## Slide 61: Control Instructions
Opcode | Operand | Description
HLT | None | Halt
The CPU finishes executing the current instruction and halts any further execution.
An interrupt or reset is necessary to exit from the halt state.
Example: HLT

## Slide 62: Control Instructions
Opcode | Operand | Description
DI | None | Disable interrupt
The interrupt enable flip-flop is reset and all the interrupts except the TRAP are disabled.
No flags are affected.
Example: DI

## Slide 63: Control Instructions
Opcode | Operand | Description
EI | None | Enable interrupt
The interrupt enable flip-flop is set and all interrupts are enabled.
No flags are affected.
This instruction is necessary to re-enable the interrupts (except TRAP).
Example: EI