## Slide 1: Unit
RISC and CISC

## Slide 2: RISC and CISC Processors
RISC stands for Reduced Instruction Set Computer and
CISC stands for Complex Instruction Set Computer.

## Slide 3
There are two approaches of the design of the control unit of a microprocessor i.e.-
Hardware approach and
Software approach.

## Slide 4: RISC Processors:-
RISC stands for Reduced Instruction Set Computer.
In Reduced Instruction Set Computer (RISC) architecture, the instruction set of the computer is simplified to reduce the execution time.
RISC has a small set of instructions, which generally include register-to-register operations.
Thus, data is stored in processor registers for computations, and results of the computations are transferred to the memory using store instructions.
All operations are performed within the registers of the CPU.

## Slide 5: Examples of RISC processors are:
DEC's Alpha 21064, 21164 and 21264 processors;
SUN's SPARC and ULTRA SPARC;
PowerPC processors etc.

## Slide 6
CISC Processors:
CISC stands for Complex Instruction Set Computer.
It comprises a complex instruction set.
It incorporates a variable-length instruction format.
Instructions that require register operands can take only two bytes.

## Slide 7
Examples of CISC processors are:
Intel 386, 486;
Pentium Pro, Pentium, Pentium II, Pentium III, Pentium 4;
Motorola's 68000, 68020, 68030, 68040, etc.

## Slide 8: Difference between RISC and CISC

## Slide 9
S.No. | RISC | CISC
1. | Simple instruction set | Complex instruction set
2. | Consists of Large number of registers. | Less number of registers
3. | Larger Program | Smaller program
4. | Simple processor circuitry (small number of transistors) | Complex processor circuitry (more number of transistors)
5. | More RAM usage | Little Ram usage
6. | Simple addressing modes | Variety of addressing modes
7. | Fixed length instructions | Variable length instructions
8. | Fixed number of clock cycles for executing one instruction | Variable number of clock cycles for each instructions